OpenWSN Abstraction Layer

Draft Specifications v0.1

Owner: Kevin Weekly

# Introduction
OpenAL is the interface for "newbie-level" interaction with the OpenWSN platform. Inspired by Arduino, mbed, etc..
# OpenMote Pinout

Drawing 1: Pin Numbering

1
10
11
20
Pin Number	LPC1758 Pin	Interrupts	Analog In	PWM	Extra Capabilities
1*	VCC				3.3V Power supply input
2	P0[2]	YES	YES	NO	UARTA TX
3	P0[3]	YES	YES	NO	UARTA RX
4	P2[7]	YES	NO	NO
5*	#RESET				Reset
6	P1[23]	NO	NO	YES	SPI MISO
7	P1[24]	NO	NO	YES	SPI MOSI
8	P1[20]	NO	NO	YES	SPI SCK
9*	#RESET				Reset ( For bootloader operation )
10*	GND				GND
11	P0[0]	YES	NO	NO	I2C SDA
12	P2[0]	YES	NO	YES	UARTC TX
13	P2[1]	YES	NO	NO	UARTC RX
14	REFP				VREF (ADC reference voltage; tie to 3.3V if not used)
15	P0[1]	YES	NO	NO	I2C SCL
16	P2[10]	YES	NO	NO	External Unmaskable Interrupt for bootloader operation
17	P1[31]	NO	YES	NO
18	P1[30]	NO	YES	NO
19	P0[26]	NO	YES	NO	UARTB RX / Analog Out
20	P0[25]	NO	YES	NO	UARTB TX

* Not capable of being GPIO
# Architecture

Drawing 2: OpenAL Software Dependencies. There may be multiple copies of the myApp task as multiple applications are installed.
myApp
OpenAL
Shared Libraries

I/O Hardware
(GPIO, ADC, DAC, PWM, UART, SPI, I2C)
OpenWSN
Network API

Resource
Arbitrator
Abstraction
 Translation

OpenAL
Groundskeeper Task

Task
Manager

myApp Task
Config
Manager
Error
Reporting
OpenWSN/ FreeRTOS APIs

OpenAL Task

Drawing 3: Program memory map on LPC17xx devices

ISRs
0x0000 0000
0x0007 FFFF
FreeRTOS/
OpenWSN
OpenAL Shared Library
OpenAL Descriptors
OpenAL Applications

User App 1
User App n

Configuration
Configuration
# API Method Prototype
### func1(param_1, param_2) func1_adv(param_1, param_2, optional_param)
Description
This function solves world hunger.

Parameters
param_1 : 32-bit number of grains of rice.
param_2 : 32-bit number of people.
optional_param : (optional) Uses this many tanks.

Returns
16-bit cost of solving world hunger.
# Utility Modules
## CONFIG (Configuration repository)
Every application should rely on this module to provide run-time configuration (i.e. sample rate, enable/disable features, etc... ). A configuration task will be run which will accept reconfiguration packages over the network.
An application will be developed to input configuration parameter descriptions and auto-generate code using this configuration mechanism as part of a template.
### config_populate(*config_struct, length)
Description
Populates the given structure with parameter data.

Parameters
*config_struct : Void pointer to C structure to be filled	with parameters
length : Length of structure in bytes

Returns
None.
## EVENTS (event detection and response)
Because applications are single-threaded and only have stack data, they must intercept interrupt events through an event system. The following types of events may be generated:
Event Name	Parameters	Description
PIN_RISING	pin_no	A GPIO pin has transitioned from LOW to HIGH
PIN_FALLING	pin_no	A GPIO pin has transitioned from HIGH to LOW
UART_RX	port	Data has been recieved on the UART
SOCK_RX		Data has been recieved on the Socket
UDP_RX		A packet has been recieved on the UDP port

### events_wait_for_event() events_wait_for_event_adv(timeout)
Description
Waits until any of the configured events are generated.

Parameters
timeout (optional) : Timeout in ms to wait before giving up.

Returns
An event structure with up to 3 parameters describing what happened:
.type = PIN_RISING, PIN_FALLING, etc...
.param1
.param2
.param3

# Core I/O Modules
## PINS (Individual Pin-Level operations)
This module covers any methods that operate on a single pin. Hence, each method has a pin variable as its first argument.
### pins_pinMode(pin, mode)
Description
Sets the specified pin mode. Disables other peripheral's control of pin.

Parameters
pin : Valid pin number
mode: One of INPUT, OUTPUT, ANALOG_INPUT, ANALOG_OUTPUT, PWM

Returns
None
### pins_digitalWrite(pin, value)
Description
Turns the specified pin on (3.3V) or off (0V). Must have been previously configured as an OUTPUT.

Parameters
pin : Valid pin number
value: HIGH or LOW

Returns
None
### pins_digitalRead(pin)
Description
Reads the digital value on the pin. Unspecified operation if the pin is configured as an analog input or output.

Parameters
pin : Valid pin number

Returns
Digital value of pin (HIGH or LOW)
### pins_analogRead(pin)
Description
Reads the analog value on the pin, referenced to VREF. Must have been configured as ANALOG_INPUT.

Parameters
pin : Valid pin number

Returns
12-bit Analog Value (0-4096). To convert to real-world volts, use V=analogRead(pin)*VREF/4096.
### pins_analogWrite(pin, value)
Description
Writes the 10-bit analog value on the pin, referenced to 3.3V. Must have been configured as ANALOG_OUTPUT (Note only pin 19 supports this)

Parameters
pin : Valid pin number
value : Analog value (0-1024).

Returns
None
### pins_pwm_write(pin, duty_cycle) pins_pwm_write_adv(pin, duty_cycle, frequency)
Description
Writes the given duty cycle on the pin.

Parameters
pin : Valid pin number
duty_cycle: floating point value, 0 being always off, and 1	being always on
frequency : (optional) changes the frequency from the default	490Hz

Returns
None
### pins_configure_pullups(pin, mode)
Description
Configures the internal pullups/pulldowns of the IO pin.

Parameters
pin : Valid pin number
mode : One of PULLUP, PULLDOWN, REPEATER, NONE.

Returns
None
### pins_configure_opendrain(pin, mode)
Description
Configures the open drain mode of the pin.

Parameters
pin : Valid pin number
mode : One of NORMAL, OPENDRAIN

Returns
None
### pins_configure_interrupt(pin, mode)
Description
Configures an interrupt on an interrupt-capable pin. Generates an event when this happens.

Parameters
pin : Valid pin number
mode : One of RISING, FALLING, BOTH

Returns
None
### pins_clear_interrupt(pin)
Description
Clears the interrupt of an interrupt-capable pin.

Parameters
pin : Valid pin number

Returns
None
## UART ( Serial TX/RX Ports)
This module operates the hardware UART module. The implementation is blocking for transmit and recieve. We use an interrupt to copy data from the RX FIFO into a temporary buffer. The advantage of blocking reads and transmit is that we can put the task to sleep when the user would likely be busy-waiting anyways.
UART recieves will generate an event every byte, unless otherwise specified.
### uart_begin(port, baud) uart_begin_adv(port, baud, rx_event_thresh)
Description
Configures a UART port. Releases pins from other modules.

Parameters
port : One of UARTA (pins 2 and 3), UARTB (pins 19 and 20),	or UARTC (pins 12 and 13)
baud : Baud rate to use on the port.
rx_event_thresh (optional) : How many bytes to recieve
(max. 64) before generating an event. A value of 0	specifies no events are generated.

Returns
None
### uart_write(port, data)
Description
Writes a char to the uart and waits for transmission to finish.

Parameters
port : UARTA, UARTB, or UARTC
data : a single byte to send

Returns
None
### uart_write(port, *buffer, length)
Description
Writes a buffer of bytes to the uart and waits for transmission to finish.

Parameters
port : UARTA, UARTB, or UARTC
*buffer : Pointer to char array to send
length : number of characters to send

Returns
None
### uart_read(port)
Description
Reads a byte of data from the uart. Blocks until available.

Parameters
port : UARTA, UARTB, or UARTC

Returns
Single byte of data from the UART
### uart_read(port, *buffer, length)
Description
Reads a buffer of bytes from the uart. Blocks until length bytes are recieved.

Parameters
port : UARTA, UARTB, or UARTC
*buffer : char buffer to copy into
length : number of bytes to expect

Returns
None
### uart_available(port)
Description
Determines the number of bytes that can be immediately read.

Parameters
port : UARTA, UARTB, or UARTC

Returns
Number of bytes that can be read without blocking.
### uart_end(port)
Description
Releases a uart port from use.

Parameters
port : UARTA, UARTB, or UARTC

Returns
None
## SPI ( 4-wire serial protocol )
This module handles the SPI hardware module. Writes are blocking and the task will sleep while waiting for write to complete.
### spi_begin(ss_pin) spi_begin_adv(ss_pin, frequency, polarity, phase)
Description
Begins master mode SPI operation on pins 6 (MISO), 7 (MOSI) and 8 (SCK). Releases pins from other peripherals.

Parameters
ss_pin : Pin to use as the slave select
frequency : Sets the communications clock frequency. Defaults	to 8MHz
polarity : ACTIVE_HIGH - SCK is active high / idle low )
     ACTIVE_LOW - SCK is active low / idle high )
phase : IDLE_TO_ACTIVE – Latch data from idle to active
  ACTIVE_TO_IDLE – Latch data from active to idle

Returns
None
### spi_write(data) spi_write_adv(data, bits)
Description
Clocks a byte over SPI and reads the result.

Parameters
data : byte to send to the slave
bits : number of bits between 8 and 16 ( default 8 )

Returns
Byte which was shifted back from the slave.
### spi_end()
Description
Releases pins 6,7, and 8 from SPI operation.

Parameters
None

Returns
None
## I2C ( 2-wire serial protocol )
This module handles the I2C hardware module. The task sleeps while waiting for writes or reads.
### i2c_begin()
Description
Begins master mode I2C operation on pins 8 (SCK) and 11 (SDA)

Parameters
None

Returns
None
### i2c_write(addr, data)
Description
Sends a byte of data to specified address.

Parameters
addr : Slave 7-bit I2C address
data : byte of data to send

Returns
None

### i2c_write(addr, *buffer, length)
Description
Sends several bytes of data to specified address. Note: not equivilant to calling i2c_write(addr,data) multiple types since it takes place in one transaction.

Parameters
addr : Slave 7-bit I2C address
*buffer : Pointer to char array to send
length : length of data buffer provided

Returns
None
### i2c_read(addr)
Description
Reads a byte of data from slave address.

Parameters
addr : Slave 7-bit I2C address

Returns
Byte of data read from slave
### i2c_read(addr, *buffer, length)
Description
Reads several bytes of data from specified address. Note: not equivilant to calling i2c_read(addr) multiple types since it takes place in one transaction.

Parameters
addr : Slave 7-bit I2C address
*buffer : Pointer to char array to read into
length : length of data to read

Returns
None
### i2c_end()
Description
Releases pins 8 and 11 from i2c operation.

Parameters
None

Returns
None
## SOCK ( TCP/IP Client socket interface )
Implements ONE client socket for an applicaton to use. Attempts to keep socket connected to remote host in the background. For multiple sockets, or server sockets, it is necessary to get closer to the metal. When bytes come in, they will be buffered for the application to grab. Otherwise, the application blocks (sleeps) until data is available.
RX events are generated every byte unless specified otherwise.
### sock_connect(addr, port) sock_connect_adv(addr, port, rx_event_threshold)
Description
Set remote host to try connecting to.

Parameters
addr : IPv6, IPv4, or name (if name resolution is enabled) of	remote host
port : port of remote host
rx_event_threshold (optional) : How many bytes to recieve
(max. 64) before generating an event. A value of 0	specifies no events are generated.

Returns
None

### sock_send(data)
Description
Send a byte of data to the remote host.

Parameters
data : The byte to send

Returns
None
### sock_send(*buffer, length)
Description
Send multiple bytes of data to the remote host.

Parameters
*buffer : Pointer to char array of data to send
length : length of data to send

Returns
None
### sock_read()
Description
Reads a byte of data from the uart. Blocks until available.

Parameters
None

Returns
Single byte of data from the socket
### sock_read(*buffer, length)
Description
Reads a buffer of bytes from the socket. Blocks until length bytes are recieved.

Parameters
*buffer : char buffer to copy into
length : number of bytes to expect

Returns
None
### sock_available(port)
Description
Determines the number of bytes that can be immediately read.

Parameters
None

Returns
Number of bytes that can be read without blocking.
### sock_close()
Description
Close TCP connection and stop trying to talk to remote host.

Parameters
None

Returns
None
## UDP (Packetized best-effort delivery)
UDP send should be used for most sensor network instances. UDP listen is good for control applications.
### udp_send(addr, port, *buffer, length)
Description
Sends a UDP packet to address.

Parameters
addr : IPv6, IPv4, or name (if name resolution is enabled) of	remote host
port : port to send on
*buffer : Data to send
length : number of bytes to send

Returns
None
### udp_listen(port)
Description
Sets up a listener on specified port. Events are generated every time a packet arrives at this port.

Parameters
port : port to listen on (1024-65535)

Returns
None
### udp_packets_available()
Description
Returns how many packets are waiting to be fetched.

Parameters
None

Returns
Number of UDP packets waiting to be fetched by udp_get_packet()
### udp_get_packet(*buffer, length)
Description
Waits for a packet to arrive or fetches the next one if available.

Parameters
*buffer : Place to put the data
length : length of the buffer ( packet is truncated if buffer	is not long enough )

Returns
Actual length of packet