## Slide 1: Security Implementation Proposal for OpenWSN
Marcelo Barros de Almeida
marcelobarrosalmeida@gmail.com

## Slide 2: IEEE 802.15.4e 2012 SECURITY
Proposal:
  Security level 5:
    Frame authentication (four bytes MIC)
    Data encryption
AES-CCM*:
  AES-128
  key length: 128 bits
  Authentication: AES-CBC-MAC
  Encryption/decryption: AES-CTR

## Slide 3: IEEE 802.15.4e 2012 FRAME
FRAME
CTRL
SEQ
NUM
DESTINATION
ADDRESS
SOURCE
ADDRESS
AUX. SEC.
HEADER
PAYLOAD
CRC
2B 1B 0-10B 0-10B 0-14B 0-16B 2B
SECURITY
CTRL
FRAME
COUNTER
KEY
IDENTIFIER
SECURITY
LEVEL
KEY IDENTIFIER MODE
FC
SUP.
1B 4B 0-9B
b7 bit6 bit5 bits 3:4 bits 0:2
KEY
INDEX
KEY
SOURCE
0-8B 1B
SECURITY ENABLE = 1
MIC
FC
SIZE
-
IE
HDR
IE
PYL
MAC HDR
MAC PAYLOAD
MAC FOOTER

## Slide 4: IEEE 802.15.4e 2012 FRAME (SEC. LEVEL 5)
SECURITY COST IS
5 BYTES
SECURITY
CTRL
1B
SECURITY ENABLE = 1
SECURITY
LEVEL
KEY IDENTIFIER MODE
FC
SUP.
bit7 bit6 bit5 bits 3:4 bits 0:2
FC
SIZE
-
1
1
Frame counter with 5 bytes and suppressed.
ASN is used as counter, from Information Elements (IE)
FRAME
CTRL
SEQ
NUM
DESTINATION
ADDRESS
SOURCE
ADDRESS
AUX. SEC.
HEADER
PAYLOAD
CRC
2B 1B 0-10B 0-10B 0-14B 0-16B 2B
MIC
IE
HDR
IE
PYL
MAC HDR
MAC PAYLOAD
MAC FOOTER

## Slide 5: AUTHENTICATION (TX/DATA)
HDR
PAYLOAD
HDR
LEN(a)
2B
PADDING
Must be divisible by 16
PAYLOAD
PADDING
Must be divisible by 16
+
AUTH DATA
=
IEEE 802.15.4 2011 - B4.1.1
SEC HDR
SEC HDR
a
m
L’= L-1 = 1 (length field size)
M’= (M-2)/2 = 1 (MIC size)
A = 1 (Auth in use)
Flags = 0x49 for security mode 5
NONCE
FLAGS
1B 13B 2B
LEN(m)
INIT. VECTOR
(B0)
=
M’
L’
A
-
bit7 bit6 bits5:3 bits0:2
SOURCE ADDRESS
FRAME COUNTER (ASN)
8B 5B
ORIGINAL FRAME:
ASN (Absolute Slot Number), is updated at each 15ms

## Slide 6: AUTHENTICATION (TX/DATA)
X0 = 0128
B0
KEY 128
AES-128
X1
B1
AES-128
X2
B(t-1)
AES-128
Xt
Bt
AES-128
Xt+1
MIC
4B 4B 4B 4B
B1
B2
B(t-1)
Bt
...
AUTH DATA
...
...
AES-CBC-MAC
INIT. VEC.

## Slide 7: ENCRYPTION (TX/DATA)
PAYLOAD
PADDING
Must be divisible by 16
ENC DATA
=
a
m
L’= L-1 = 1 (length field size)
M’= 0 (No MIC)
A = 0 (No auth)
Flags = 0x01 for security mode 5
NONCE
FLAGS
1B 13B 2B
CNT
A0, A1, A2, ...
=
M’
L’
A
-
bit7 bit6 bits5:3 bits0:2
Counter = 0, 1, 2 ...
SOURCE ADDRESS
FRAME COUNTER (ASN)
8B 5B
HDR
PAYLOAD
SEC HDR

## Slide 8: ENCRYPTION (TX/DATA)
A0
KEY 128
AES-128
S0
A1
AES-128
C1
A(t-1)
AES-128
C(t-1)
At
AES-128
Ct
E. MIC
4B 4B 4B 4B
MIC
M1
M(t-1)
M t
...
C1
C2
C(t-1)
Ct
...
ENCRYPTED PAYLOAD (LEFTMOST m OCTETS)
ENCRYPTED PAYLOAD
E. MIC
HDR
CRC
SEC HDR
M1
M2
M(t-1)
M t
...
ENC DATA
FINAL FRAME:
PAD.
...
...
AES-CTR

## Slide 9: DECRYPTION (RX/DATA)
C1
C2
C(t-1)
Ct
...
ENCRYPTED PAYLOAD
E. MIC
HDR
CRC
SEC HDR
ENCRYPTED PAYLOAD
E. MIC
PADDING
Must be divisible by 16
L’= L-1 = 1 (length field size)
M’= 0 (No MIC)
A = 0 (No auth)
Flags = 0x01 for security mode 5
NONCE
FLAGS
1B 13B 2B
CNT
=
M’
L’
A
-
bit7 bit6 bits5:3 bits0:2
Counter = 0, 1, 2 ...
SOURCE ADDRESS
FRAME COUNTER (ASN)
8B 5B
AES-CTR
INPUT
PARAMETERS
PAD. (12B)
AES-CTR
OUTPUT
DECRYPTED PAYLOAD (LEFTMOST m OCTETS)
DECRYPTED PAYLOAD
DECRYPTED MIC (LEFTMOST 4 OCTETS)
D. MIC
A0, A1, A2, ...

## Slide 10: AUTHENTICATION (RX/DATA)
HDR
LEN(a)
2B
PADDING
DECRYPTED PAYLOAD
PADDING
+
AUTH DATA
=
SEC HDR
L’= L-1 = 1 (length field size)
M’= (M-2)/2 = 1 (MIC size)
A = 1 (Auth in use)
Flags = 0x49 for security mode 5
NONCE
FLAGS
1B 13B 2B
LEN(m)
=
M’
L’
A
-
bit7 bit6 bits5:3 bits0:2
SOURCE ADDRESS
FRAME COUNTER (ASN)
8B 5B
AES-CBC-MAC
INPUT
PARAMETERS
C. MIC
AES-CBC-MAC
OUTPUT
DECRYPTED
D. MIC
CALCULATED
If C.MIC and D.MIC are the same, accept the frame
INIT.
VECTOR
(B0)

## Slide 11: HARDWARE SUPPORT
Radio | Crypto Engine | Mode of Operation | Project
CC1100 | No | - | WSN430 1.3b
CC2420 | Yes | ECB, CBC, CTR, CBC-MAC, CCM | TelosB, WSN430 1.4b, Z1, MICAz, EPIC
CC2520 | Yes | ECB, CBC, CTR, CBC-MAC, CCM, CCM* | CC2531EMK
CC2430/CC2530 | Yes | ECB, CBC, CTR, CBC-MAC | -
CC2538 | Yes | ECB, CBC, GCM, RSA, CTR, CCM | OpenMote, USP Mote
AT86RF230 | No | - | RAVEN, IRIS
AT86RF231 | Yes | ECB, CBC | GINA, IoT LAB M3, deUSB2400, XpressoHach, OpenMoteHack
MC13213 | Yes | EBC | USP Mote
MC13224 | Yes | CBC, CTR | -
STM32W108 | Yes | CTR, CCM, CBC-MAC, CCM | OpenMoteSTM. Agilefox (?)
EM357 | Yes | CTR, CBC-MAC, CCM, CCM* | -
JN5148 | Yes | CTR, CBC, CCM* | -